7.3 CHECKS AND INSPECTIONS

Inspections

In accordance with its certification, the PEAK 5 must be periodically serviced. An inspection must be scheduled every 100 flying hours or every 24 months, whichever comes first.

We strongly recommend that any repairs should be performed in a specialist repair shop by qualified personnel.

This is the only way to guarantee the airworthiness and continued certification of your PEAK 5.

A thorough pre-flight check must be performed before every flight.

Trim check

The PEAK 5 is fitted with unsheathed lines. Their durability conforms to unsheathed line standards. Their strength is guaranteed and their resistance to UV is one of the highest in this type of lines.

However, using these lines means there is a requirement to maintain the trim of your PEAK 5 within the stipulated ranges.

In general terms, the lengths of the lines change during the operational life of the wing.

We recommend checking the lines after the first +/- 30 flying hours.

Why is this necessary?

Thanks to our research and experience acquired over time by our R&D team, we are capable of predicting how lines will perform.

By following the stipulated maintenance schedule and inspections the wing remains at optimum trim without any loss of performance.

The maintenance carried out on each wing will be different depending on the conditions of each flying area, climate, temperature, humidity, type of terrain, wing load, etc. With regard to the so-called “loops”,

some models are delivered with loops already made. To adjust the trim these can be loosened or readjusted.

However, a wing should not be trimmed according to the measurements copied from another wing of the same type. Each trim setting is individual to each wing, and is determined after measurements and subsequent analysis by specialized personnel.

Trim adjustments must be within 1% of the length allowed by the certification.

7.4 REPAIRS

We recommend any inspection or repair is performed by a Niviuk professional in our official workshop: http://niviuk.com/content/service.

Any modification of the glider made in an unauthorised workshop will invalidate the guarantee of the product. Niviuk cannot be held responsible for any issues or damage resulting from modifications or repairs carried out by unqualified professionals or who are not approved by the manufacturer.

8.	SAFETY AND RESPONSIBILITY

It is well known that free-flying with a paraglider is considered a high-risk sport, where safety depends on the person who is practicing it.

Incorrect use of this equipment may cause severe, life-changing injuries to the pilot, or even death.

Manufacturers and dealers cannot be held responsible for your decisions, actions or accidents that may result from participating in this sport.

You must not use this equipment if you have not been properly trained to use it.

Do not take advice or accept any informal training from anyone who is not properly qualified as a flight instructor.

9.	GUARANTEE

The equipment and components are covered by a 2-year warranty against any manufacturing defect.

The warranty does not cover misuse of the equipment.

Any modification of the paraglider or its components invalidates the guarantee and its certification. The following are not considered to be modifications:

Replacement of damaged parts

Trim correction

Repairs

Partial or total line replacement.

The above must all be carried out according to the parameters stipulated by NIVIUK and in accordance with its certification.